## Slide 1
Digital Twin-Enabled AI Framework for Predictive Maintenance
Product Lifecycle Optimization of Heavy Equipment Engine Components
📚 COURSE: ME4506 – Product Lifecycle Management (PLM)
👨‍🏫 FACULTY MENTOR: Dhanesh Babu
👥 PROJECT TEAM: Thirumalairajan U & Tharunkumar RP

## Slide 2
ME4506 – PRODUCT LIFECYCLE MANAGEMENT
Project Abstract & Problem Context
⚠️ Limitations of Conventional Maintenance
• Extreme Engine Stress: High mechanical loads, continuous vibration, and thermal pulses accelerate bearing and piston wear.
• Reactive Maintenance: Fixes components after catastrophic failure, incurring average $48,000+ repair costs and unplanned downtime.
• Preventive Maintenance: Fixed-schedule servicing leads to premature replacement of healthy components.
💡 Proposed AI + Digital Twin Framework
• Digital Twin Virtualization: Real-time telemetry monitoring (Temp, Vibration, Oil Pressure, RPM, Load, Duty Hours).
• Parallel Machine Learning: Random Forest Classifier (96.67% accuracy) & RUL Regressor (R² = 0.97).
• PLM Decision Layer: Converts AI predictions into 3 actionable lifecycle decisions (Operate, Maintain, Replace).

## Slide 3
ME4506 – PRODUCT LIFECYCLE MANAGEMENT
Project Key Objectives & Scope
Objective 1: Dataset Engineering
Build a synthetic/real sensor dataset (1,200 records) reflecting realistic engine degradation physics and operational stress parameters.
Objective 2: Machine Learning Models
Train a Random Forest classifier for health state prediction (Healthy, Warning, Failure) and a regressor for Remaining Useful Life (RUL) estimation.
Objective 3: Digital Twin Dashboard
Develop an interactive Streamlit digital twin dashboard to mirror physical component state, displaying RUL gauges, ISO 10816 vibration classes, and CAD wear maps.
Objective 4: PLM Decision Integration
Integrate AI outputs directly into a PLM decision layer to recommend Operate, Maintain, or Replace actions with financial ROI cost optimization.

## Slide 4
ME4506 – PRODUCT LIFECYCLE MANAGEMENT
Digital Thread Telemetry Pipeline Architecture
1. Edge Telemetry
Temp, Vibration, Oil Press, RPM, Load, Hours
2. Data Preprocessing
StandardScaler & LabelEncoder (Python)
3. ML Inference Engine
Random Forest Classifier & RUL Regressor
4. Digital Twin Dashboard
Real-Time Telemetry & ISO 10816 Diagnostics
5. Enterprise PLM
PTC Windchill sBOM Export & ECR Actions

## Slide 5
ME4506 – PRODUCT LIFECYCLE MANAGEMENT
Machine Learning Performance & Validation
🎯 Classifier Results (Random Forest)
• Accuracy: 96.67% • Weighted Precision: 96.71% • Weighted Recall: 96.67% • F1 Score: 96.68% Confusion Matrix:
Failure Healthy Warning Failure 67 0 3 Healthy 0 68 2 Warning 3 0 97
📈 RUL Regressor Results (Random Forest)
• Mean Absolute Error (MAE): 42.40 hours • Root Mean Sq Error (RMSE): 54.80 hours • R² Score: 0.9717 (97.17% Variance Explained) Key Insights: • High precision RUL estimation enables proactive maintenance scheduling 150+ hours prior to catastrophic failure hazard.

## Slide 6
ME4506 – PRODUCT LIFECYCLE MANAGEMENT
ISO Engineering Standards Compliance
ISO 10816 / ISO 20816 – Mechanical Vibration Severity
Monitors non-rotating bearing vibration velocity (mm/s): • Class A: Good / Excellent (< 2.8 mm/s) • Class B: Acceptable Operation (2.8 - 7.1 mm/s) • Class C: Unsatisfactory (7.1 - 11.2 mm/s) • Class D: Damage Hazard (> 11.2 mm/s)
ISO 4406 – Fluid Cleanliness Rating
Quantifies solid particle contamination per mL across 3 size thresholds (≥4µm / ≥6µm / ≥14µm). High particle counts correlate with bearing spalling and cylinder scuffing.
ISO 13374 & ISO 23247 – Digital Twin Standards
Standardized Condition Monitoring architecture (Data Acquisition → State Detection → Health Assessment → Prognostics RUL → Advisory Generation).

## Slide 7
ME4506 – PRODUCT LIFECYCLE MANAGEMENT
Digital Twin Telemetry Dashboard Features
🌐 Live Telemetry
Real-time health status badges (Healthy 🟢, Warning 🟡, Failure Risk 🔴) & confidence scores.
📊 RUL Gauge Indicator
Visual Plotly gauge tracking remaining operational hours against overhaul thresholds.
🧩 Subsystem Wear Map
Dynamic wear index computation for Crankshaft Bearings, Pistons, Oil Pump, and Turbocharger.
🎛️ Simulation Modes
Pre-configured operational stress tests (Thermal Overload, Vibration Fault, Lubrication Starvation).

## Slide 8
ME4506 – PRODUCT LIFECYCLE MANAGEMENT
Explainable AI (XAI) & Generative AI Copilot
🔍 Feature Importance (XAI)
• Quantifies mathematical feature weights to identify principal degradation drivers. • Identifies primary failure mechanisms (e.g. vibration velocity or oil pressure drop). • Generates automated plain-English diagnostic evaluations for engineers.
🤖 Generative AI Copilot & RCFA
• Interactive AI Chatbot: Answers custom technical questions on bearing repair & PLM strategy. • Root Cause Failure Analysis (RCFA): Recommends exact overhaul kits (PM-250, PM-1000, PM-3000). • Google Gemini API Support with intelligent offline engineering fallback.

## Slide 9
ME4506 – PRODUCT LIFECYCLE MANAGEMENT
PLM Decision Layer & Financial ROI Optimizer
1. Operate (Healthy 🟢)
Continue standard operation & PM-250 servicing.
2. Maintain (Warning 🟡)
Schedule inspection within 150 hrs & PM-1000 overhaul.
3. Replace (Failure 🔴)
Initiate replacement planning & PM-3000 emergency kit.
💰 Financial ROI & Enterprise PLM Integration (PTC Windchill)
• Cost Savings: Preventative maintenance (₹1,20,000) vs catastrophic engine failure (₹35,00,000) yields ₹33,80,000+ net PLM savings. • PTC Windchill Export: One-click export of Service Bill of Materials (sBOM.csv) containing part numbers and live AI health state. • Closed-Loop Digital Thread: Connects As-Designed CAD definition with As-Operated field telemetry.

## Slide 10
ME4506 – PRODUCT LIFECYCLE MANAGEMENT
Conclusion & Future Scope
✅ Project Conclusion
• Successfully built an AI-driven Digital Twin framework for heavy equipment engines. • Achieved 96.67% health classification accuracy & 0.97 R² RUL regression score. • Closed the loop between sensor telemetry and PLM decision making, shifting maintenance from reactive to fully predictive.
🔮 Future Scope
1. Edge AI Microcontrollers: Deploying quantized ONNX models on engine ECU edge hardware. 2. Physics-Informed Neural Networks (PINN): Coupling thermodynamic equations with deep learning. 3. Direct SAP / Siemens Teamcenter API Connectors: Automated work-order dispatch via MQTT/REST.